## Slide 1: Lecture 06
Integer Codes

## Slide 2: Binary Codes
Goal: To translate data and instructions (human understandable) into binary (machine understandable), and back again.
Questions:
How are operators encoded?
How are operands encoded?
  data
How is arithmetic performed?
  add/sub/imul/div
  comparison
  addresses
: int
, float
, characters
: int
instruction

## Slide 3: Binary Representation of Integers
What does 1001 11012 mean?
use positional value, just like for decimal.
Decimal: 658
Binary: 1001 1101
27
1s
10s
100s
= 100
= 101
= 102
= 6×102 + 5×101 + 8×100
(Expanded Notation)
20
21
22
23
26
25
24
= 1×27 + 0×26 + 0×25 + 1×24 + 1×23 + 1×22 + 0×21 + 1×20
= 27 + 24 + 23 + 22 + 20
= 128 + 16 + 8 + 4 + 1
= 15710
unsigned [integer]
representation
Range of possibilities?
1 byte:
n-bit:
[0, 255]
[0, 2n − 1]
A fixed-length encoding has a fixed number of possibilities.
Notes: Always a good question to ask HOW they arrive at 2n - 1

## Slide 4: Conversions Between Binary and Decimal
1
decimal → binary?
two methods
Method 1: Continual Subtraction
Strategy: Continually subtract the largest power of 2.
E.g., 157 =
binary → decimal?
seen it already:
=
1
1
= 27 + 24 + 23 + 22 + 20
expand and sum!
Scratch work:
157
128
29
+ 16
13
+ 8
5
+ 4
1
+ 1
1
1
0
0
0
Works well for small numbers, but not for, say, 1 293
660
421.

## Slide 5: Method 2: Continual Division [by 2]
1 0 0 1 1 1 0 . 1
0
Strategy: Continually divide by 2.
1 0 0 1 1 1 0 1
Accumulate the remainders in reverse order.
Quotient Remainder
157 -
78 1
39 0
19 1
9 1
4 1
2 0
1 0
0 1
Q. Why does this work?
Obs: Dividing a binary number by 2:
shifts all bits right by one, and . . .
the remainder was the 1’s bit
idiv 2
remainder
divide again

## Slide 6: Other Common Bases
Hexadecimal (base 16)
digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
binary ↔ hex?
Partition the number into groups of 4 bits, starting from the right.
Translate each group of 4 into its hex value.
E.g., 15710
= 1 0 0 1 1 1 0 1 2
10
11
12
13
14
15
the inverse procedure also works
Binary ↔ octal (base 8)?
Same procedure, but groups of 3 bits
E.g., chmod 644 a2.pdf
= 9D16
9
D
→ rw-/r--/r--
Notes: Each group of 4 bits is 24 more significant than the last one.

## Slide 7: Binary Arithmetic
Arithmetic algorithms can be adapted to binary
Rule: If it happens every ten in decimal, it should happen every two in binary.
Addition:
Decimal:
6 5 8
+ 1 5 1
8
0
9
1
Rule: Carry if total ≥ ten
Binary:
1 0 0 1 1 1 0 1
+ 0 0 1 0 1 1 0 0
Rule: Carry if total ≥ two
1
1
1
1
0
0
0
0
1
1
1
1
verify in decimal
1 5 7
+ 4 4
2 0 1?

## Slide 8: Overflow
Binary:
1 1 1 1 1 1 1 1
+ 0 0 0 0 0 0 0 1
Occurs when the expected result falls beyond the range.
Decimal:
9 9 9
+ 1
0
0
0
1
1
0
0
0
0
0
0
0
0
1
1
1
1
2 5 5
+ 1
2 5 6
1
need an extra digit
1
1
1
1
Rule: For unsigned addition, an overflow occurs when there is a carry out of 1 from the most significant column.
256 is not representable in 8-bit
⇒ 255 + 1 = 0
carry out