## Slide 1: Lecture 08
Overflows and Condition Codes

## Slide 2: Overflow Rules
−2n + 1,
sub
[
]
2n + 1 − 2
0,
[
An overflow occurs when the result of a computation falls out of range, i.e., makes no sense.
Unsigned
Addition:
Subtraction:
[0, 2n − 1]
[0, 2n − 1]
add
]
  overflow if ≥ 2n, i.e., if the carry out of the most significant bit (MSB) is 1.
2n − 1
[0, 2n − 1]
[0, 2n − 1]
  overflow if < 0, i.e., if the carry out of MSB is 0.
  See Assignment 3.
Notes: Addition may cause overflow off the high end of the range. Subtraction, off the low end.

## Slide 3: Overflow Rules
−2n,
add
[
2n − 2
2’s Complement Addition:
[−2n − 1, 2n − 1 − 1]
[−2n − 1, 2n − 1 − 1]
]
  overflow if sign changes unexpectedly.
E.g.,
(−100) + (−100)
50 + 100
~ too negative!
result = 56
~ too positive!
result = −106
Quick Test: A 2’s complement overflow occurs if and only if the carry in to the MSB differs from the carry out of the MSB.
Notes: Addition may cause overflow off the high end of the range. Subtraction, off the low end.

## Slide 4: Overflow Examples
50 + 100:
0 0 1 1 0 0 1 0
+ 0 1 1 0 0 1 0 0
1
1
5010 = 0 0 1 1 0 0 1 02
10010 = 0 1 1 0 0 1 0 02
−5010 = 1 1 0 0 1 1 1 02
−10010 = 1 0 0 1 1 1 0 02
(−100) + (−100):
100 + (−50):
1
0
0
0
0
0
1
1
1
1
0
carry in ≠ carry out
⇒ overflow
1
0
0 1 1 0 0 1 0 0
+ 1 1 0 0 1 1 1 0
1
0
0
0
0
0
1
1
1
1
1
carry in = carry out
⇒ no overflow
1
1
1
1
1 0 0 1 1 1 0 0
+ 1 0 0 1 1 1 0 0
0
0
0
0
1
0
1
1
1
carry in ≠ carry out
⇒ overflow
0
1
1
1
1

## Slide 5: x86-64 Condition Codes
Several single-bit registers describe attributes of the most recent arithmetic operation or comparison.
test using conditional jumps
CF: Carry Flag
ZF: Zero Flag
SF: Sign Flag
OF: Overflow Flag
- operation caused unsigned overflow
- operation resulted in zero
- operation yielded a negative value
- operation caused a 2’s complement overflow

## Slide 6: Bitwise Operations
0 = false; 1 = true
each operation works by column
can and a bitmask
can xor a bitmask
x86-64
and
or
not
xor
C
&
|
~
^
to test if certain bits are set
to toggle specific bits
E.g., andb %cl, %al
al: 1 1 0 1 1 0 0 1
cl: 0 1 1 0 0 0 0 0
C: a = a & c; or a &= c;
new al: 0 1 0 0 0 0 0 0
bitmask
The only bits that survive are where the bitmask is 1.
E.g., xorb %cl, %al
al: 1 1 0 1 1 0 0 1
cl: 0 1 1 0 0 0 0 0
C: a = a ^ c; or a ^= c;
new al: 1 0 1 1 1 0 0 1
The only bits that change are where the bitmask is 1.

## Slide 7: Shifting
Slide bits left/right by k places
E.g., shl $2, %al
al: 0 0 1 0 1 1 0 0
x86-64
shl/sal
shr
sar
C
<<
>>
>>
C: a = a << 2; or a <<= 2;
new al: 1 0 1 1 0 0 0 0
  arithmetic effect:
multiply by 2k
Shift left can replace mul by constant
for some constants only!
time for shift/logic/add/sub << mul << div
another method: leal (%eax, %eax, 4), %eax
eax + 4•eax → eax

## Slide 8: shr vs sar
Similarly, shift right should divide by 2k
shr: logical shift right
sar: arithmetic shift right
- zero fill
- sign fill
E.g., shr $2, %al
al: 1 1 0 1 1 1 0 0
new al: 0 0 1 1 0 1 1 1
(220)
(55)
effect: div by 2k (unsigned)
E.g., sar $2, %al
al: 1 1 0 1 1 1 0 0
new al: 1 1 1 1 0 1 1 1
(−36)
(-9)
effect: div by 2k (signed)