## Slide 1: Lecture 09
Where to Store Fixed Data

## Slide 2: Bitwise Application: abs(x)
≡ −x
This is what gcc produces:
movl %edi, %edx
sarl $31, %edx
movl %edx, %eax
xorl %edi, %eax
subl %edx, %eax
Compare this to the 4-line version:
movl %edi, %eax
testl %eax, %eax
jns endabs
negl %eax
endabs:
ret
x is +ve
edx is
all 0’s
eax is
x
eax is
x
x is −ve
all 1’s
x
x + 1
runs about 8% slower on CSIL machines
branching is less predictable
see later: pipelining

## Slide 3: Storing Data in Memory
Two Methods
fixed memory
dynamic memory
Fixed Memory
declare using a label & a directive for size
  label:
  size:
  initial value
  dedicated purpose through life of program
(stack)
  temporarily use and recycle
  lasts through life of function call
as a shorthand for the address
.byte, .word, .long, .quad
1
2
4
8
C:
long a = 5;
long b = 8;
void main {
. . .
}
x86-64:
b: .quad 8
a: .quad 5
. . .
Byte order is least significant in least address
M[]
08
00
00
00
00
00
00
00
05
00
00
00
00
00
00
00
b:
a:
“little Endian”
Notes: Demo mainline-max

## Slide 4: Arrays
Both refer to array
address a is the
In C, a pointer is a
address of a[i] =
In C, you can increment a pointer
*(a + i) =
a: .quad 8
.quad 10
.quad 12
vs. a: .quad 8, 10, 12
long a[3] = {8, 10, 12};
base address
base address & a type
type ⇒ size of object (L)
base + i • L
adds L to the address
a[i]

## Slide 5: Other Common Directives
.float, .double, .string
.align [248]
sets the next declaration at the next available address that’s a multiple of 2/4/8
it’s recommended, but not required.
  Why?
Because of the layout of memory.
. . . as you would expect
- “word boundaries”
RAM
address
control
64
data
Interface:
supply an address x, in binary
wait
read/write up to 8 bytes at addresses
[x, x + 1, x + 2, …, x + 7]

## Slide 6: Binary Prefixes
When x is a multiple of 8, its binary equivalent ends in −000.
M[]
11111
11101
11011
11001
10111
10101
10011
10001
01111
01101
01011
01001
00111
00101
00011
00001
11110
11100
11010
11000
10110
10100
10010
10000
01110
01100
01010
01000
00110
00100
00010
00000
x + 1 ends in −001
x + 2 ends in −010
...
x + 7 ends in −111
common prefix
Memory is most efficient when operating on bytes with a common prefix
code still works without .align 8, but you may have to pay 2 accesses for 1 piece of data (slower)