## Slide 1: Lecture 22
Computers as State Machines

## Slide 2: Recall
Combinational circuits
can compute any function
costs time
no memory
Nature of hardware:
Strategy: Design multi-functional components and use control wires to
: inputs ⟼ outputs
: propagation delay
, i.e., outputs based only on current inputs
can’t adjust wiring while executing
select a function

## Slide 3: Registers
CPU-centred memory
retains n bits over time
Reg-n
Load
CLK
D
Q
n
n
(state)
controlled by Load wire
synchronized by system-wide clock
Spec:
Q broadcasts
D inputs
State changes
Load = 0
A system-wide clock sends 01010101…
clock period = duration for 1 full cycle
clock frequency = 1/period
current state
next state
only on the rising edge of the clock (↑)
disables all state changes

## Slide 4: Timing
  inputs
  current state
next state is a function of
function table:
algebraic description:
Load D Q(t + 1)
  Q(t + 1) = Load • D + Load • Q(t)
clock period =
370 ps
Clock
Load
D
Q
0
1
1
1
1
0
0
0
clock frequency = 1 / 370 × 10−12 s
= 2.70 × 109 Hz
= 2.7 GHz
tpd for register
next state
current state
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A & B
...
current state
1 1 1
0
X
Q(t)
0 0
1

## Slide 5: Computers as State Machines
Algorithms usually require memory to hold state information, from step to step.
Recall: Finite State Machines (CMPT 125)
0
Σ = {0, 1}
1
0
0
1
1
ends
with a
single 1
ends
with 11
next state is computed based on
add a memory tape
current state + next input
⇒ Turing machine
Accepts all binary strings that end in “11”.

## Slide 6: Digital State Machines
Memory holds state information
memory
combinational
circuit
current
state
inputs
next state
outputs
compute next state based on (current state, inputs)
compute outputs based on (current state, inputs)
Q. What does this imply about the clock period?
clock period must exceed tpd of combinational circuit + tpd of registers

## Slide 7: Staged Execution
In the programmer’s model, each elementary command changes the state.
E.g., addq %rbx, %rbp
movq %rax, (%rdi, %rcx, 4)
In digital systems, each command is broken up into a sequence of several stages, one cycle per stage
fetch (F)
decode (D)
calc (C)
memory (M)
write back (W)
however, one clock cycle per instruction ⇒ very large cycle
- IR ← M[PC]
- prepare operation, load all operands
- compute result
- access memory
- update registers