## Slide 1: Lecture 25
Pipelining Hazards

## Slide 2: Recall
Divide assembly instructions into substates
five stages:
D
C
M
W
F
increase throughput by overlapping different stages of different instructions
  pipelining
resource conflicts may lead to data inconsistency
  insert pipeline stalls (bubbles)

## Slide 3: Load/Use Data Hazard (Read After Load)
E.g., I1: movmr 0(r5), r2
I2: add r2, r4
movmr 0(r5), r2
D
valA ← r2
(10)
valB ← r4
(13)
State: r2: 10
r4: 13
r5: 0x4948
M[0x4948]: 29
→ 29
→ 42
F
D
C
M
add r2, r4
W
F
C
M
W
valA ← r5
(0x4948)
valC ← disp
(0)
valE ← valA + valC
(0x4948)
valE ← valB + valA
(23)
r2 ← valM
(29)
r4 ← valE
(23)
data forwarding doesn’t solve it. Why not?
  value ready during phase 4, but needed during phase 3
a stall (one bubble) is required
valM ← M[valE]
(29)

## Slide 4: Stalling vs Interleaving
Stall the instruction, and it’s as if the instruction starts one cycle later
code optimization:
F
D
C
M
W
D
C
M
W
F
Φ
valM ←
M[valE]
(29)
valA ← r2
(29)
movmr 0(r5), r2
add r2, r4
F
D
C
M
W
D
C
M
W
F
D
C
M
W
F
movmr 0(r5), r2
add r2, r4
interleave with independent instruction
add $4, r5
Notes: If you do it in the order A-C-B, it will be like 4 instructions due to the hazard

## Slide 5: Structural Hazard
Memory is asked to read two memory locations at once
F
D
C
M
W
D
C
M
W
F
movmr 0(r5), r1
add r2, r4
D
C
M
W
F
D
C
M
W
F
add r3, r6
add r7, r5
valM ← …
IR ← …
two solutions:
  stall the fourth instruction
  redesign memory (it’s slow anyway)
Notes: If you do it in the order A-C-B, it will be like 4 instructions due to the hazard

## Slide 6: Branch [Mis-]prediction & Penalties
Q. When the next instruction in the pipeline is a branch, which instruction should be fetched next?
either inc(PC) or PC + disp, depending on condition codes (FLAGS)
result of branch not known until end of phase 4
I1: cmp r1, r2
I2: jle loop
I3: movrr r3, r2
I4: add r5, r2
not taken
taken
last calculation
F
F
F
F
D
C
M
W
D
C
M
W
D
1
2
3
4
5
6
C
speculative
execution
F
F
D
  I3 and I4 are squashed, i.e, changed into bubbles
  mispredicting branches ⇒ loss of cycles
✗
✗
Branch Prediction
usually 90+% correct
Heuristics:
branch backward; fall forward (65-75%)
statistical methods
machine learning (AI methods)
Notes: Typical hardware will lose 10-20 cycles, mostly due to longer pipelines.