## Slide 1: Lecture 26
Multiple Instructions per Cycle

## Slide 2: Recall
Divide each assembly instruction into stages & parallelize
Resource conflicts can waste cycles
Today: Further Hardware Optimizations
x86-64 uses pipelining to increase CPU performance, in combination with several other strategies
(pipelining)
complete one instruction per cycle for shorter cycle
stall instructions
squash instructions
(data or structural hazards)
(mispredicted branches)

## Slide 3: Out of Order Execution (OoOE)
Strategy: Fetched instructions are placed in a queue and any data dependencies (hazards) among them are computed. The instruction control unit (ICU) selects an eligible instruction on each cycle to be run by the execution unit (EU).
instructions may be run out of order
E.g., Program Order
movmr 0(r5), r2
add r2, r4
add $4, r5
program order vs data order
table of data dependencies ensure the same results
data
dependency
(+1 bubble)
movmr 0(r5), r2
data dependency does not allow I2 to run immediately after I1
  run I3 instead!
add $4, r5
add r2, r4
Data Order
⟼
Notes: In general, OoOE operates by having a processor that computes dependencies among instructions. There are many ways to do this, including by keeping track on a scoreboard, or by having a very rudimentary dependency graph. The length of the instruction queue has limits because of this . . . the complexity of the circuit does not scale linearly with the size of the queue.

## Slide 4: Multiple Operations per Clock Cycle
The story so far:
a scalar processor
Vector Processing (AVX-SSE)
operate on 1-D arrays (vectors)
E.g., x86-64: vmulps %xmm0, %xmm1, %xmm2
SSE: Streaming SIMD Extensions
SIMD: Single Instruction stream, Multiple Data streams
SISD: Single Instruction stream, Single Data stream
1 clock cycle ↔ 1 operation
want less than 1 cycle per operation
xmm0:
xmm1:
xmm2:
2.8
6.3
−1.2
−42.0
15.4
−30.24
−7.2
−0.0
=
=
=
=
×
×
×
×
127
95
63
31
0
32
64
96
5.5
−4.8
6.0
0.0
4 muls at once!
also ymm / zmm regs (256 / 512-bit)
also 64-bit values
float / double or int / long
Notes: AVX-SSE stands for Advanced Vector eXtensions / Streaming SIMD eXtensions. SIMD (pronounced sim-dee) stands for “single instruction stream, multiple data streams”, i.e., executing one instruction at a time, but on vectors. A scalar processor is an example of SISD (single instruction stream, single data stream). MIMD and MISD are also possible, usually involving multiple processors in parallel, but MISD is very uncommon. MIMD would be a multi-core, superscalar architecture, or perhaps a distributed system.
SIMD are used predominantly in digital signal processing applications and graphics processing. Those of you who play games or stream games need these vector instructions for high performance. Rob Cameron, based at Surrey, uses these to process XML files quickly.

## Slide 5: Superscalar
Strategy:
E.g., Intel Core i7 Haswell:
# Functions
0 add, div, fmul, fdiv, branching
1 add, mul, fadd, fmul
2, 3 load, address computation
4 store
5 add
6 add, branching
7 address computation for store
multiple function units
may assign one instruction to each unit
Can assign up to:
4 integer adds at once
2 floating point muls
2 loads
Notes: Orally: 8 function units are usually the limit due to concurrency overhead vs payoff

## Slide 6: Loop Unrolling
Strategy:
E.g.,
total = 0;
for (i = 0; i < n; i++) { total += A[i];
}
Restructure code to allow multiple adds at once.
sum[2] = {0,0};
for (i = 0; i < n-2; i += 2) { sum[0] += A[i];
sum[1] += A[i+1];
}
total = sum[0] + sum[1];
for (; i < n; i++) {
total += A[i];
}
Data dependency:
each total depends on the previous total
must do each add in sequence
two sequences of adds
  each independent from the other