## Slide 1: Lecture 17
Intro to Instruction Set Architectures

## Slide 2: Instruction Set Architectures (ISA)
A formal specification of the set of instructions the CPU can execute
Elements:
memory
  word size
  size of external memory
  size of internal memory
set of instructions
set of data types
requirements spec. for hardware
assembly programmer’s model
(RAM)
(registers)
+ physical formats (binary layout)
+ physical formats (binary encodings)

## Slide 3: Anatomy of Instructions
4c 03 00
7e fb
c3
4c 03 00
7e fb
c3
Assembly language:
a symbolic rep’n of instructions
  human readable
  extras: mnemonics, labels, directives
loop: addq (%rax), %r8
jle loop
ret
Machine language:
each instruction has an equivalent binary encoding
opcode
Format:
opcode
operands
mnemonics:
operands:
symbolic rep’n of opcode
some are implicit, some explicit
different addressing modes are possible
bits that represent the opcode
bits that encode all explicit operands
Notes: Demo: do an objdump on these three instructions. It’s instructive to do two things: 1. Figure out why “fb” on the jle instruction. 2. Figure out why it’s 18 on the addq instruction.

## Slide 4: ISA Philosophy
Goals:
each instruction shall have an unambiguous encoding
functional completeness
instruction sets may be small or large
RISC:
small # of general purpose instructions
CISC:
large # of instructions including special purpose instructions
CPU can unambiguously decode and execute them
Turing-completeness and Turing tarpits
Reduced Instruction Set Computing
  < 100
small # of instructions
  smaller machine instructions
  simpler CPU design
Complex I.S.C.
  performance gains from customizing CPU for special instructions
  more instruction variety may reduce need for subprograms
ARM
MIPS
x86
Notes: RISC purists didn’t even have MUL or DIV - were programmed as subroutines.
These days, most machines are blended in their philosophies . . . the best of both worlds

## Slide 5: Machine Instruction Formats
Templates to encode entire instruction set
Principles:
E.g., Let “add a, b, c” be an assembly instruction that means M[c] ← M[a] + M[b].
Suppose that external memory is 212 × 16.
Q. What would be a reasonable instruction format?
Use only a few formats.
Fields in different formats that have the same purpose should appear in the same position.
Assign opcodes to all instructions.
Determine sizes of all operands.
# of words
word size
in bits

## Slide 6: E.g., add a, b, c meaning M[c] ← M[a] + M[b]
  3 bits
Opcode size?
E.g., Let there be 13 instructions. What’s the opcode size?
depends on # of instructions for the whole system
Operands?
format must include
Rule: A set of n values requires log2n bits.
  4 bits
⇒ up to 23 opcodes
⇒ up to 24 opcodes
Format?
3 explicit addresses
(12 bits each)
must hold 4 + 3 × 12 = 40 bits
✗
✓
⇒ at least 3 words per instruction
physical format:
word 1
word 2
word 3
OPC
Dst c
15
12
11
0
Src a
Src b
11
0
11
0
Notes: You COULD put a, b, c in a different order, but we’ll see later that this is a good order.