## Slide 1: Lecture 18
The von Neumann Bottleneck

## Slide 2: Instruction Set Architecture (ISA)
Recall:
ISA describes
each instruction must have a unique encoding
the functions of the CPU
  instruction format (template)
  opcode & operand encoding

## Slide 3: E.g., 3-Operand Machine
13 instructions
212 × 16 external memory
3-operand instruction: add a, b, c (meaning: M[c] ← M[a] + M[b])
XXXX
XXXX
physical format:
word 1
word 2
word 3
OPC
Dst c
15
12
11
0
Src a
Src b
11
0
11
0
⇒ 4 bits/opcode
⇒ 12 bits/address
sample code:
z ← (x + y) * (x - y)
opcode table
add: 0001
sub: 0010
mul: 0110
add x, y, tmp1
sub x, y, tmp2
mul tmp1, tmp2, z
0001
addr of x
addr of y
addr of tmp1
?
?
X is for “anything”
0:
Addr
XXXX
XXXX
0010
addr of x
addr of y
addr of tmp2
3:
XXXX
XXXX
0110
addr of tmp1
addr of tmp2
addr of z
6:
Notes: It’s probably a good seat exercise to ask the class to fill in the bits for sub and mul

## Slide 4: Evaluating ISAs: The von Neumann Bottleneck
Q. How good is the design?
The von Neumann Bottleneck:
during fetch phase
during decode phase
during execute phase
depends largely on the number of memory accesses
each instruction must be retrieved from memory
External memory access is the slowest, most constrained aspect of instruction execution.
a limitation on the transfer rates between memory & CPU across the bus
some instructions will read/write memory
explicit operands may lengthen machine instructions
Notes: You may wish to draw the black box diagram of a computer to refresh their memory on the various pieces and how the bus fits into the picture.

## Slide 5: E.g., 3-Operand Machine (cont’d)
E.g., How many accesses for z ← (x + y) * (x - y)?
add x, y, tmp1
sub x, y, tmp2
mul tmp1, tmp2, z
A total of 18 memory accesses are required.
Possible improvements?
add registers and operate on values only in registers
  smaller addresses to fetch
  fewer accesses on execute
fetch + decode
execute
3
3
3
3
3
3
(or 4)

## Slide 6: E.g., 3-Operand Machine w/Registers
movrr rA, rC
movmr a, rC
movrm rA, c
, movrm
addr a
13 instructions
212 × 16 external memory
23 × 16 registers
addr a/c
The ISA:
- movmr
movrr rA, rC
movmr a, rC
movrm rA, c
Semantics:
(r0 ↔ r7)
add rA, rB, rC
sub rA, rB, rC
mul rA, rB, rC
rC ← rA + rB
rC ← rA - rB
rC ← rA * rB
rC ← rA
rC ← M[a]
M[c] ← rA
formats:
OPC
15
12
11
Dst C
Src A
Src B
9
8
6
5
3
- add, sub, mul
15
12
11
Dst C
Src A
9
8
6
OPC
11
0
Opcode:
0001
0010
0110
1001
1010
1011
, movrr
Notes: Q. How many bits to encode a register?
Q. Which instructions will use the first instruction format? Note the compactness on movrr
Q. How to build the second instruction format?

## Slide 7: Sample Code: z ← (x + y) * (x - y)
movmr x, r1
movmr y, r2
add r1, r2, r3
sub r1, r2, r4
mul r3, r4, r5
movrm r5, z
addr of x
0001
011
001
010
001
1010
XXXX
XXXXXXXXX
XXX
f + d
exec
2
1
2
1
1
0
1
0
1
0
2
1
Total = 12