## Slide 1: Lecture 19
Shortening Instructions

## Slide 2: Instruction Set Architecture (ISA)
Recall:
Instruction sets must be:
functionally complete
unambiguously encoded
  opcode & operands
  several instruction formats
Minimize effect on von Neumann bottleneck
Goal:
fetch
decode
execute
minimize instruction length
− operate on regs instead of mem

## Slide 3: E.g., 3-Operand Machine w/Regs (Previous Lecture)
13 instructions
212 × 16 external memory
23 × 16 registers (r0 ↔ r7)
addr a
addr a/c
- movmr, movrm
add rA, rB, rC
sub rA, rB, rC
mul rA, rB, rC
movrr rA, rC
movmr a, rC
movrm rA, c
rC ← rA + rB
rC ← rA - rB
rC ← rA * rB
rC ← rA
rC ← M[a]
M[c] ← rA
formats:
OPC
15
12
11
Dst C
Src A
Src B
9
8
6
5
3
- add, sub, mul, movrr
15
12
11
Dst C
Src A
9
8
6
OPC
11
0
9 words for fetch/decode & 3 words for execution of z ← (x + y) * (x - y)
Q. How to shorten instructions?
Notes: Q. How many bits to encode a register?
Q. Which instructions will use the first instruction format? Note the compactness on movrr
Q. How to build the second instruction format?

## Slide 4: Strategies to Reduce Instruction Size
Strategy 1:
save the operand
simpler CPU design
reduces expressiveness
Strategy 2:
an addressing mode describes
seen so far:
  direct mode:
  register mode:
⇒ save its bits
⇒ longer programs
Assignment 6
?
3-Operand ⟼ 2-Operand Machine
Add more addressing modes
how the explicit operands are interpreted
indicates the external memory addr of the value to be used
indicates the register addr of the value to be used
Q. What other modes are possible?
(12)
(3)
Notes: Orally: A couple of good points to be made. 1. Direct mode costs a memory access on execute, but register mode does not. 2. How many bits does each field count for in our running example? (12/3). How much do they count for in x86-64? (32/4)

## Slide 5: Immediate Mode
Operand indicates actual value to be used.
trade-off:
format:
add $value, rC
movi $value, rC
rC ← rC + value
rC ← value
magnitude of value vs instruction size
0000
1000
OPC
15
12
11
Dst C
9
8
0
value
OPC
15
12
val8-3
Dst C
5
3
value
Alt:
val2-0
only 9 bits for value
  range:
  sign-extension:
, but target is 16-bit
[−256, 255]
copy bit 8 into bits 15..9
Notes: The “Alt:” is for the alternative universe where we put the register operands in the order A-B-C instead of C-A-B.

## Slide 6: Indirect Mode & Base + Displacement Mode
Alt:
base + displacement mode:
format:
register indirect mode:
format:
mov (rA), rC
mov rA, (rC)
rC ← M[rA]
M[rC] ← rA
indicates a register containing external addr of the value
1100
1101
OPC
15
12
11
Dst C
9
8
OPC
15
12
val5-3
Dst C
5
3
val2-0
Src A
6
mov value(rA), rC
mov rA, value(rC)
rC ← M[rA + value]
M[rC + value] ← rA
indicates a register (base addr) and a value (displacement), whose sum (effective addr) is the external addr of the value
1110
1111
OPC
15
12
11
Dst C
9
8
Src A
6
0
5
value
range:
[−32,31]
Src A
11
9
8
6
2
0
Notes: You could just use base + displacement for register indirect mode, but with a zero displacement.
Note that in x86-64, the 64-bit mode doesn’t allow direct addressing. Instead, they use base+displacement from the instruction pointer. Thus the offsets for the same fixed memory address will differ depending on where in the code you are

## Slide 7: Sample Code: z ← (x + y) * (x - y)
movi $x, r7
mov 0(r7), r1
mov (y-x)(r7), r2
add r1, r2, r3
sub r1, r2, r4
mul r3, r4, r5
mov r5, (z-x)(r7)
f + d
exec
1
0
1
1
1
1
1
0
1
0
1
0
Total = 10
1
1
computed at compile time, not run time
Notes: Extra demo: SIB encoding in x86-64.