## Slide 1: Lecture 21
Combinational Circuits

## Slide 2: CPU Organization
Goal: Given an instruction set architecture, construct a machine that reliably executes instructions.
Design choices will influence speed of instructions:
some instructions will be faster than others
order of instructions may matter
order of memory access may matter
“conflicts” or “hazards”

## Slide 3: Black Box Architecture
A black box is employed to abstract the function of a device.
Notation:
values of 0/1 travel along wires (lines)
arrows indicate direction of travel
there are inputs and outputs
input x
input y
output z
OR gate
z = x | y
Also:
AND
XOR
After a change in inputs, there is a time delay for outputs
≕ propagation delay (tpd)
on a picosecond to nanosecond scale
find longest distance from inputs to outputs

## Slide 4: Mystery Circuit : Full Adder
function table:
  basically a truth table
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
1
1
1
3-bit
Addition!
0
1
1
0
1
0
0
1
A
B
C
Q. What’s the propagation delay?
C
S
3 gate delays (highlighted)
Q. What does the circuit accomplish?
algebra:
S = A ^ B ^ C
; C = (A & B) | (C & (A ^ B))
S = A ⊕ B ⊕ C
; C = AB + C(A ⊕ B)
C S
Full Adder
Half Adder
Half Adder
FA
S
C
C
A
B

## Slide 5: Computing with Combinational Circuits
its outputs react only based on its inputs. There are no feedback loops and no state information (memory) is maintained.
Definition: A combinational circuit computes a pure function, i.e.,
Theorem: Every Boolean function can be implemented
using a combinational circuit composed of and / or / not / xor.
black box designs can be modular
FA
FA
FA
FA
A3
B3
A2
B2
A1
B1
A0
B0
S3
S2
S1
S0
C3
C2
C1
C0
C4
… a 4-bit ripple carry adder!
  adds by columns
  propagation delay
= 9
(2n + 1)
Adder-4
A
B
4
4
4
S
C
C
Notes: Orally: We used to spend ⅔ of CMPT 150 on the design techniques to minimize circuit size, gate delay, etc …
The point in CMPT 295 is only that it is possible to do so, and that gate delay is a thing
Orally: This is why additions is slow. And why mul is even slower.
Orally: How to make an Adder-8?

## Slide 6: Function Unit
32
Hardware circuits are fixed
can’t adjust wires/gates while running
build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A & B
...

## Slide 7: Function Unit: Adder-Subtractor
32
Adder-32
32
32
A
32
B
S
C
FS
if FS == 0 then
S = A + B
if FS == 1 then
= A − B
S = A + B + 1