## Slide 1: Lecture 23
Staged Execution

## Slide 2: Recall
next state
algorithms require memory
computers are very large finite state machines
memory
combinational
circuit
current
state
inputs
outputs
Note:
clock cycle is a factor in CPU throughput
e.g., if register load time is 20 ps and the combinational circuit’s delay is 400 ps, what is max throughput?
  min clock cycle =
  max throughput =
400 + 20
shorter cycle ⇒ higher throughput
1 instruction / 420 ps
(state information)
  compute next state as a function of current state + inputs
  state changes synchronized by system-wide clock (↑)
= 420 ps
= 2.4 billions of instructions per second
GIPS

## Slide 3: Reducing Cycle Times
Strategy: Divide each assembly instruction into stages
Five Stages:
fetch (F)
decode (D)
calculate (C)
memory (M)
write back (W)
build a combinational circuit to perform each stage
perform one stage per cycle
may use extra registers to save information between stages
D
current
state
C
M
W
F
next
state
current
state
F
D
C
M
W
Original:
New:
time
next
state
20 ps
add 80 ps, but may not have to do all stages

## Slide 4: The Five Stages
Some upgrades to the ISA:
machine is 2-operand
opcode is 8-bit
save copy of the current instruction
save intermediate calculations
dst ↔ r[B], src ↔ r[A]
parsed by (class, func)
in IR (instruction register)
in valX registers
fetch (F)
  load next instruction
decode (D)
  prepare operation (function select)
  load all operands
calculate (C)
  compute result
memory (M)
  access external memory (read/write)
write back (W)
  update state (registers)
IR ← M[PC]
valA ← r[A], valB ← r[B], valC ← const
valE ← valB op valA (or valC)
valM ← M[valE] or M[valE] ← valA
r[B] ← valE

## Slide 5: Some Example Instructions
Decode (D)
E.g., movrr r4, r6
OPC
valA ← r[4]
Dst C
Src A
Src B
0 1 1 0 0 0 0 0
1 1 0
1 0 0
X X
1 1 0
1 0 0
X X
0 1 1 0 0 0 0 0
dst
src
opcode
Fetch (F)
IR
0 1 1 0
0 0 0 0
IC
func
(mov)
(r → r)
Instruction Class
1 1 0
1 0 0
B
A
(6)
(4)
Write back (W)
r[6] ← valA
Notes: Good to ask the audience to encode dst and src!
In this example, you should do the first two steps and then ask them for the third.

## Slide 6: add r3, r5
valA ← r[3]
Decode (D)
valB ← r[5]
Fetch (F)
OPC
Dst C
IC
Src A
Src B
0 1 1 0 0 0 0 0
1 1 0
1 0 0
X X
1 0 1
0 1 1
X X
1 0 0 1 0 0 1 0
dst
src
opcode
IR
1 0 0 1
0 0 1 0
func
(op)
(add)
1 0 1
0 1 1
B
A
(5)
(3)
Write back (W)
r[5] ← valE
Calc (C)
valE ← valB + valA
Note: Neither of the first two examples used all 5 stages.
Notes: Good to ask the audience to encode dst and src!
In this example, you should do the first two steps and then ask them for the third.

## Slide 7: movmr 8(r3), r1
Write back (W)
r[1] ← valM
(0x00440408)
Calc (C)
valE ← valA + valC
valA ← r[3]
Decode (D)
Fetch (F)
OPC
Dst C
IC
Src A
Src B
0 1 1 0 0 0 0 0
1 1 0
1 0 0
X X
0 0 1
0 1 1
X X
0 1 1 0 1 1 0 1
dst
src
opcode
IR
0 1 1 0
1 1 0 1
func
(mov)
(m → r)
(base+disp)
0 0 1
0 1 1
B
A
(1)
(3)
0 0 0 0 1 0 0 0
disp8
0x00000008
(8, sign extended)
valC
(0x00440410)
Memory (M)
valM ← M[valE]
Notes: Good to ask the audience to encode dst and src!
In this example, you should do the first two steps and then ask them for the third.