## Slide 1: Lecture 24
Pipelining

## Slide 2: Recall
Divide assembly instructions into substates
five stages:
D
C
M
W
F
pay small overhead per stage, but large savings if you save a stage
Problem: It may be difficult to find equal cost stages

## Slide 3: Pipelining
Strategy: Overlap different stages of different instructions
Program:
serial execution ⟼ pipelined execution
Serial
Pipelined
time
time
D
C
M
W
F
D
C
M
W
F
D
C
M
W
F
D
C
M
W
F
D
C
M
W
F
D
C
M
W
F
I1:
I3:
I2:
I1:
I2:
I3:
C
D
F
M
C
D
Notes: Will animate the transition from the yellow state to the pink state on the next slide

## Slide 4: Pipelining Design
Strategy: Build a combinational circuit that computes each stage.
I3 (F)
I2 (D)
I1 (C)
I4 (Start)
I1 (M)
I4 (F)
I3 (D)
I2 (C)
Comb.
Circuit
W
Comb.
Circuit
F
Comb.
Circuit
D
Comb.
Circuit
C
Comb.
Circuit
M
Start of Phase 4
…
…
…
…
…
…
…
…
End of Phase 4
…
…

## Slide 5: Q. What is the impact on throughput?
CPU throughput:
Cost per instruction
E.g., Suppose each stage of an instruction propagates in 100 ps and a register requires 20 ps to load. What is the throughput with and without pipelining?
Cost per instruction
CPU throughput
Serial
Pipelined
= 5 × 100
+ 20
= 520 ps
CPU throughput
= 1 instruction
/ 520 ps
= 1.92 GIPS
in general, CPU throughput = 1 / cycle time
  = 1 / 120 ps in the pipelined example above
= 5 × 100
+ 5 × 20
= 600 ps
= 1 instruction
/ 600 ps
= 8.33 GIPS
) × 5
Instruction latency:
× 1.15
× 4.33
(

## Slide 6: Limitations on Pipelining
E.g., What would the CPU throughput be on a 10-stage pipeline?
In the best case, each stage now costs
CPU throughput
More stages result in diminishing returns
50 + 20
= 70 ps
= 1 / 70 ps
= 14.3 GIPS
Doubling the stages didn’t double the throughput.
limiting behaviour as n → ∞
  Assignment 7
Notes: Orally: Modern processors have 15+ stages to reduce clock cycle times.

## Slide 7: Resource conflicts may delay the pipeline
D
valA ← r1
(15)
valB ← r5
(17)
E.g., I1: add r0, r1
I2: add r1, r5
State: r0: 10
r1: 15
r5: 17
→ 25
→ 42
add r0, r1
F
D
C
M
add r1, r5
W
F
C
M
W
valA ← r0
(10)
valB ← r1
(15)
valE ← valB + valA
(25)
valE ← valB + valA
(32)
r1 ← valE
(25)
r5 ← valE
(32)
Problem: I2 needs value of r1 computed by I1, but not written back until phase 5.
data
dependency

## Slide 8: Solution 1: Stall the pipeline for I2
D
valA ← r1
(15)
valB ← r5
(17)
add r0, r1
F
D
C
M
add r1, r5
W
F
C
M
W
valA ← r0
(10)
valB ← r1
(15)
valE ← valB + valA
(25)
valE ← valB + valA
(32)
r1 ← valE
(25)
r5 ← valE
(32)
Solution 2: Forward the data calculated in the pipeline. (data forwarding)
add r0, r1
F
add r1, r5
D
C
M
W
D
C
M
W
F
Φ
Φ
Φ
r1 ← 25
stalls or bubbles
valA ← r1
(25)
add r0, r1
bubble (nop)
bubble
bubble
add r1, r5