## Slide 1: Lecture 29
Memory Hierarchy, Locality

## Slide 2: Recall
Can optimize / refactor C code based on:
pipelining
multiple function units
optimization blockers
But also:
structure of memory
  take advantage of locality
avoid data hazards
, reduce branch misprediction
unroll / reduce loops to take advantage of CPU parallelism
reduce memory aliases
, function calls

## Slide 3: Registers vs Memory
DRAM is big, but slow
  waiting 60 cycles per access is impractical
  both fetch & memory stages would have to be expanded
 | reg | mem
Caching
Strategy:
takes advantage of
  recent memory references will be referenced again soon
  memory nearby recent memory references will be referenced soon
0.33 ns
20 ns
≈ kilobyte
≈ gigabyte
access time
size
(60×)
(~ 106×)
Strategy: Also use a smaller, faster memory (SRAM)
  1.3 ns
(4×)
from the French “cacher”
- to hide / cover
Store commonly used memory references in SRAM
locality principle:
(temporal locality)
(spatial locality)
applies to both data & code
Notes: Orally: Both regs and mem have sped up considerably over the decades, but the speed gap has WIDENED to 60x.
Orally: Explain the 90/10 rule . . . that 90% of the time is spent running 10% of the code.

## Slide 4: E.g., Good vs Bad Spatial Locality
int A[N][N];
int i, j, sum;
sum = 0;
for (i = 0; i < N; i++) { for (j = 0; j < N; j++) { sum += A[i][j];
}
}
int A[N][N];
int i, j, sum;
sum = 0;
for (i = 0; i < N; i++) { for (j = 0; j < N; j++) {
}
}
“stride-1”
(sequential)
“stride-N”
… c30
… c20
… c10
0x607c00
A30
A31
A32
A33
A20
A21
A22
A23
A10
A11
A12
A13
A00
A01
A02
A03
sum += A[j][i];
N = 4:
A30
A31
A32
A33
A20
A21
A22
A23
A10
A11
A12
A13
A00
A01
A02
A03
“row-major”
(+1 each step)
“column-major”
(+N each step)
Principle: Stride-k patterns have better locality and generally outperform stride-(k+1) patterns.
A00
A00
Notes: Demo this for various [large] N

## Slide 5: Memory Hierarchy
No Caching
CPU
Registers
Main Memory
(DRAM)
CPU
Registers
Cache
(SRAM)
Main Memory
(DRAM)
holds a small number of values for calculations
holds program
text & data
~ 60 cycles
per access
~ 4 cycles
per access
~ 60 cycles
per access
Caching
holds a subset of main memory
Cache holds several lines, each 64 bytes
each line can hold a copy of 64 bytes from main mem (or be empty)
CPU interacts with cache instead of main mem
if line in cache, data is served (cache hit)
if line is not in cache, cache must load it from main mem (cache miss)