## Slide 1: Lecture 30
Cache Particulars

## Slide 2: Recall
takes advantage of locality:
speed separation between registers (1 cycle / access) and DRAM (60 cycles / access) is huge
Strategy: use a faster SRAM (4 cycles / access) to hold a copy of
a portion of main memory likely to be used in the near future
≕ the cache
temporal
- access the same location again soon
spatial
- access a nearby location soon

## Slide 3: Cache Parameters
Q. What’s the capacity of this cache?
4 sets
E.g., (S, E, B, m) = (4, 2, 64, 48)
E.g., (S, E, B, m) = (4, 2, 64, 48)
E.g., (S, E, B, m) = (4, 2, 64, 48)
Caches come in all shapes and sizes
Definition: Let M = 2m be the size of memory (m bits / address). A cache is composed of
each set contains
each line holds:
E.g., (S, E, B, m) = (4, 2, 64, 48)
S = 2s cache sets, where
E cache lines
B = 2b bytes of data
≕ blocking factor
a valid bit
t tag bits
(where t = m − (b + s))
Set 0 {
Set 1 {
Set 2 {
Set 3 {
64 bytes
tag
V
block
40
1
× 2 lines / set
× 64 bytes / line
= 512 bytes
in general: capacity C =
S × E × B
Notes: Q. What’s the tag size?

## Slide 4: Address Translation
supply addresses of length m:
CPU interacts with cache instead of main memory
set index indicates
check for matching tag
if cache hit:
if cache miss:
t
s
b
tag
set index
block offset
in which set to look
acts as a hash function
⇒ cache hit / miss
access offset in cache line
  load block from main memory
  evict a block (if none empty)
  access offset in new cache line

## Slide 5: E.g., (S, E, B, m) = (4, 2, 64, 48)
cache miss:
  load memory 0x6120c0 ↔ 0c6120ff into set 3: tag ← 0x6120; valid ← 1
  access 56th byte
cache hit:
  examine set 3
cache miss:
  load memory 0x6106c0 ↔ 6106ff into set 3
0x6106c8
Set 0 {
Set 1 {
Set 2 {
Set 3 {
tag
V
block
001000
11
0110000100000110
set 3
8th byte
tag = 0x6106
001000
11
0110000100000110
0x6106d4
  tag ← 0x6106
0x6106
1
; valid ← 1
  access 8th byte within block
8th
010100
11
0110000100000110
set 3
20th byte
tag = 0x6106
010100
11
0110000100000110
0x6120f8
  matching tag!
  access 20th byte within block
20th
111000
11
0110000100100000
set 3
56th byte
tag = 0x6120
111000
11
0110000100100000
  if set full, then must evict a line in set 3
← 6 →
-2-
← 40 →
Notes: Q. What’s the tag size?

## Slide 6: Eviction Strategy
Evict the line least likely to be used in near future
Random:
Least Recently Used (LRU):
Least Frequently Used (LFU):
Select line randomly
fast & easy to implement in H/W
no locality advantage
Select line accessed furthest in the past
must maintain access stats
⇒ more H/W
Select line referenced fewest times recently
again, more stats ⇒ more H/W